## Slide 3: The use of MACC curves to define policy instruments for low carbon growth

## Slide 4: Energy Forecasting Framework and Emissions Consensus Tool (EFFECT)
Developed by the World Bank
Excel-based, engineering-style, bottom-up tool with some built-in optimization
A consensus-building tool, designed to be used by multiple stakeholders
Designed to facilitate a transparent sharing of data and assumptions

## Slide 5: Current modules
Transport
Industry
Power
Households
Non-residential
Transport includes road, rail, waterborne, and air transportation of people and goods

## Slide 6: EFFECT Ecosystem
The EFFECT Model
Freely downloadable from the World Bank (http://esmap.org/EFFECT)
Easily customizable to local requirements
e-Learning Courses
Extensive self-paced training course (https://olc.worldbank.org/content/low-carbon-development-planning-modelling-self-paced).
Over 2000 practitioners trained by the World Bank in facilitated courses

## Slide 7: Usage
Power Sector
  India, Nigeria, Thailand, Philippines, Malaysia, Indonesia, Vietnam
Transport (on-road)
  10 city-level studies:
    Addis Ababa, Bangkok, Beijing, Chengdu, Guangzhou, Hanoi, Ho Chi Minh City, Jakarta, Manila, Ulaanbaatar
  Country-level Low Carbon Development studies:
    India, Brazil ,Poland, Georgia, Nigeria, Vietnam, Macedonia
    Malaysia, Indonesia, Thailand, Philippines
Household electricity
  India, Thailand, Philippines, Malaysia, Indonesia, Vietnam
Nonresidential and Industry
  India, Vietnam

## Slide 8
Ribbon navigation, analysis and help

## Slide 9
Easy to understand, adaptable, modifiable

## Slide 10: Household Module Methodology
Uses Household (HH) Consumption Survey data to separate HH by location (Rural, Urban) into 100 quantiles each, ordered by per-capita income
Projects HH size, expenditure, and number of households per quantile from census and survey data to 2050
Forecasts electrified households
Analyzes ownership and use of 17 appliance type categories by HH quantile
Applies an appliance stock model and new appliance forecasts to model changes in energy efficiency
Determines electricity consumption and marginal abatement costs

## Slide 11
1. National household size
Distribution of household size, expenditure and number
Historic development
Historic number of households
Macro Scenario
GDP
Urbanization
Population
2. Household size projection by location
Historic 15-64 age-group population size
Historic annual rate of ratio change
Mean rural household size
Number of rural household / year
Mean urban household size
Number of urban households / year
Rural population
Total population / year
Projected fraction of
urban households
3. Baseline centiles
4. Per capita income projection
Monthly per capita expenditure (MPCE)
/ 100 quantiles (centiles)
Rural-urban migration
Annual rural MPCE
/ centile
Annual urban MPCE
/ centile
6. Projected household expenditure
Mean monthly household expenditure (MMHE)
Number of households / centile
5. Adjustment of household size
Adjustment factor
Weighted mean urban household size
/ centile
Weighted mean rural household size
/ centile
MPCE growth projections
Total number of households / year
Mean national household size
Household size distribution / centile
Number of rural households / centile
Number of urban households / centile
Notes: The darker blue boxes are related to rural

## Slide 12
Household size
projection
Identification of electrified households
1. Electrified households
Per capita income projection
Rural-urban migration
Annual rural MPCE / centile
Annual urban MPCE / centile
MPCE growth projections
Macro Scenario
GDP
Urbanization
Population
Total population / year
Total number of households / year
Mean national household size
Household electrification program
Predicted electrification rate
Number of electrified urban households / centile
Number of electrified rural households / centile
I
I
Notes: The transparent boxes indicate previous steps

## Slide 13
Appliance ownership and active population
Projected household expenditure
Mean monthly household expenditure (MMHE)
Electrified households
Household electrification program
Predicted electrification rate
Number of electrified urban households / centile
Number of electrified rural households / centile
1. Appliance ownership
Number of
appliance-owning urban households
/ centile
2. Number of appliances in use
Projected active population
Annual replacement
Growth in active population
Mortality calculations
New appliance sales volumes / year
Projected number of appliances / household
Projected active appliance population / year
Number of
appliance-owning rural households
/ centile
Total number of appliances in use
/ centile
Total number of appliances in use
/ centile
I
II

## Slide 14
Electric consumption from households
Projected active population
Annual replacement
Growth in active population
Mortality calculations
New appliance sales volumes / year
Projected active appliance population / year
2. Electricity consumption
Total projected electricity consumption from households
1. Lighting
Projected urban electricity consumption from lighting
Historic electricity consumption from lighting
Predicted use of individual appliances
Energy efficiency levels
Projected rural electricity consumption from lighting
III

## Slide 15: Power Sector Module Methodology
Projects the demand for electricity to 2050 from sectoral analyses
Evaluates supply options from captive generation, T&D loss reduction and grid supply
Builds a detailed database of operating and planned generating units over the 40 year framework
Determines on a scenario basis, new generating units to be built by model to meet selected criteria. Model includes 67 on- and off-grid generating technologies
Analyzes best policy mix to make plant-build attractive to private investors
Conducts each year the load dispatch of available plants on a merit order low variable cost basis to cover demand
Calculates economic and financial outputs for each plant type by year and marginal abatement costs

## Slide 16
Power Module
Techno-Economic Modelling Framework
Demand
Transmission & Distribution
Scenario Analysis
Investment Schedule
Operating & Maintenance
GHG Emissions
Supply
Load Dispatch Calculation
T & D Losses
Plant Assignation
Current Capacity
Additional Capacity
Electricity Generation
Output
Results
Off-grid power production on site
Assumed to use fuel oil for generators
New Plants
Low Carbon Plants
Traditional Plants
Energy Efficiency
Units
Existing Plants
Planned Plants
Captive Generation
Grid Demand
Macro Scenario
Input
Household
Non-Residential
Industry
Transport
Supply needed
To be supplied to Grid
Each
Year
41 yrs
Plant Dispatch
GDP
Urbanization
Population
Load Duration Curve
Discount
Rate
Shortages
Spinning Reserves
Notes: The Energy Efficiency box does not go there. Grid demand is defined by user demand for electricity less off-grid or captive energy supply
Additional Capacity should be Required Additional Capacity
Mention load duration curves
In plant characteristics, capacity is important.
Why highlight Supply and System-wide per year?
Discount Rate should not be included (does not merit a box)

## Slide 17: Currently includes 45 technologies plus an additional 22 off-grid technologies …and easy to add more and modify
Binary
500 MW
Dual Flash
500 MW
SingleCycle
500 MW
Dual Flash
50 MW
Binary
300 MW
Dual Flash
500 MW
SingleCycle
500 MW
Dual Flash
500 MW
Wind
Nuclear
Biomass/gas
PHWR
1350 MW
PWR
1200 MW
Hydro
Storage
300 MW
Run-of-river
300 MW
Pumped
500 MW
Onshore
100 MW
Offshore
100 MW
Landfill gas
5 MW
Biomass MSW
20 MW
Solar
PV
5 MW
Thermal
30 MW
Thermal-store
30 MW
Geothermal
Binary
20 MW
Dual Flash
50 MW
Oil
SingleCycle
150/250 MW
Combined
450 - 800 MW
Steam
300 MW
Gas
SingleCycle
150/250 MW
Combined
450 - 800 MW
Steam
500 MW
Diesel
ICE
250 MW
Coal
IGCC
500 MW
IGCC + CCS
500 MW
CFB Supercrit
500 MW
CFB Subcrit
300 MW
Subcritical
300 MW
Supercritical
500 MW
Super + CCS
500 MW
Ultracritical
500 MW
Key
imported
national

## Slide 18: Transport Module Methodology
Calculates and forecasts private vehicle ownership and use from HH survey data by location (Rural, Urban) in each of 100 quantiles, ordered by per-capita income
Evaluates passenger and freight commercial vehicle ownership and usage
Analyses other surface transport modes for passengers and freight (urban, suburban and long-distance rail; inland waterways and coastal shipping).
Evaluates modal shift in country-wide studies where traditional four-step transport model does not exist
Disaggregates vehicles into 250 emissions categories and applies advanced vehicle stock model and new technology forecasts to calculate: Fuel consumption, GHG and local emissions CO, VOC, NOx, PM
Calculates economic and financial outputs for each vehicle class by year and marginal abatement costs

## Slide 19
Aviation Passenger & Freight
Transport
Modeling
Framework
Private vehicle ownership and use
On-road mass passenger transport
On-road freight transport
All vehicles
Efficiency and Emissions
Inland waterways and coastal
Rail passenger and freight transport

## Slide 20
1. Projected Urban/Rural household vehicle ownership
Private, commercial & governmental vehicle ownership & use
Average household size
2. Baseline population of additional vehicles
Total active vehicle population in baseline year
7. Baseline ridership
Average no. of passengers per vehicle
3. Total baseline vehicle population
Disaggregated by e.g.
Historic vehicle sales data / year
Macro Scenario
GDP
Urbanization
Population
Vehicle mortality calculations / year
Baseline survey of in-use vehicles
No. of households
Household expenditure
5. Projected population changes
Market development info
Vehicle sales mix / year
Annual replacement
Vehicle sales volumes / year
6. Projected use patterns
Average km travelled per vehicle related to age / year
4. Projected active population
Mix of use patterns
Type (subtype)
Engine displacement
Technology
Gross vehicle weight
Age
Fuel use
Baseline passenger-km travelled
Non-household ownership of vehicles
8. Projected travel distance
Vehicle-km travelled / year
Modal shift assump-tions
Household ownership of vehicles
Total active vehicle population / year
Change to vehicle population mix / year
Baseline vehicle-km travelled
Per capita income projections
Future passenger-km travelled / year
Mortality calculations
Passenger cars and Two-wheelers
Income per 100 quantiles
Notes: In step 1: The darker framed boxes illustrates two sets of data (for rural and urban)
In steps 4-8: The underlying boxes illustrates that the projections are performed for the disaggregated population
In step 4 and 8: The orange circles indicates that this information is used in next steps for other passenger transport
For all: The inverted boxes indicates the ‘result’ of the given step

## Slide 21
1. Baseline vehicle population
On-road mass passenger transport
Disaggregated by e.g.
Historic vehicle sales data / year
Vehicle mortality calculations / year
Baseline survey of in-use vehicles
Type (subtype)
Engine displacement
Technology
Gross vehicle weight
Age
Fuel use
2. Baseline ridership
Baseline passenger-km travelled
Baseline vehicle-km travelled
Total on-road passenger-km travelled
Baseline private passenger-km travelled
3. Projected use patterns
Average km travelled per vehicle related to age / year
Mix of use patterns
Macro Scenario
GDP
Urbanization
Population
4. Projected travel distance
Total on-road passenger-km travelled / year
Future non-private passenger-km travelled / year
Modal shift assumptions
Future private passenger-km travelled / year
6. Projected population changes
Market development info
Vehicle sales mix / year
Annual replacement
Vehicle sales volumes / year
Change to vehicle population mix / year
Mortality calculations
Average no. of passengers per vehicle
Light duty commercial vehicles, busses and coaches
5. Projected active population
Total active vehicle population / year
Future vehicle-km travelled / year
Private Vehicle Ownership& Use
Notes: In step 2 and 4: The turquoise boxes indicates information taken from previous steps

## Slide 22
5. Projected vehicle sales mix
Macro Scenario
GDP
Urbanization
Population
1. Baseline vehicle population
Disaggregated by e.g.
Historic vehicle sales data / year
Vehicle mortality calculations / year
Baseline survey of in-use vehicles
Type (subtype)
Engine displacement
Technology
Gross vehicle weight
Age
Fuel use
3. Projected use patterns
Average km travelled per vehicle related to age / year
Mix of use patterns
4. Projected travel distance
Total on-road freight tonne-km travelled / year
Modal shift assumptions
6. Projected vehicle population changes
Market development info
Vehicle sales mix / year
Annual replacement
Vehicle sales volumes / year
Change to freight vehicle population mix / year
Mortality calc.
2. Baseline freight transported
Baseline freight tonne-km travelled
Baseline vehicle-km travelled
Average load per vehicle
Load capacity
7. Projected active population
Total active freight vehicle population / year
Future vehicle-km travelled / year
On-road freight transport
Light, medium and heavy duty vehicles, trucks and tractor-trailers
Average load per vehicle

## Slide 23
1. Projected operating conditions
For all vehicles
Local operating conditions
Driving conditions
Bio-fuel mix
Vehicle load & road grade
Average trip length
Inspection & maintenance
Ambient temperature
3. Baseline emissions and fuel consumption
COPERT4
Empirical data
4. Calibration to local conditions
Local fuel consumption / road test results
Correction factor
Total emission factors
(CO2/km)
Fuel consumption
5. Projected reference emissions and fuel consumption
Total vehicle emissions / year
6. Projected change in efficiency
Projected change in vehicle efficiency
MAC curves for distinct vehicle types
7. Projected low carbon emissions and fuel consumption
2. Vehicle expenditure
New vehicle purchase cost
In-use vehicle operating costs
Total fuel consumption / year
Total vehicle emissions / year
Total vehicle-km travelled by all vehicles / year
Total active vehicle population / year
Total fuel consumption / year
Total vehicle-km travelled by all vehicles / year
Total active vehicle population / year
Private vehicle ownership and use
On-road mass passenger transport
On-road freight transport
Efficiency and Emissions
Notes: Step 1, 4 and 5: The mid-tone colour indicates that these contain projections also for the baseline year.
Step 6 and 7: The green colour indicates that this is performed for the low carbon scenario.

## Slide 24: Currently includes: 250 vehicle types/technologies 28 Low Carbon technologies plus TDM & “soft” measures …and easy to add more
2W:- Mopeds, scooters, and
motorcycles
3W :- All
PC :- Mini, Small, Lower Medium,
Medium and Upper Medium,
Large and Luxury, SUV
LCV :- AUV/MUV
Mini van/truck, pick-up, van
HCV :- Urban Bus by GVW range
Coach by GVW range
Rigid Truck by GVW range
Tractor-trailer by GCW range

## Slide 25
Freight
Passenger
Rail passenger and freight transport
1. Base-year use patterns
Average kms travelled per passenger and freight-ton
Mix of use patterns
Macro Scenario
GDP
Urbanization
Population
On-road private and mass-transit travel mix
Metro and Light Rail
High-speed
Passenger Rail
Main-line & Commuter Passenger Service
Main-line & Dedicated Freight Service
Electrified
Diesel-electric
2. Projected travel distance
Electrified / non-electric mix
Future passenger-km and freight-ton km travelled / year
Modal shift assumptions
Future Expansion plans
Future Pass & Freight movements
5. Projected wagon and locomotive population usage and changes
Annual replacement
Unit sales per year
Mortality calc.
Load capacity
Fuel Efficiency
Per unit
3. Loading Factors
Total car & wagon usage
4. Train
configuration
Car/Wagon per train
Locomotive & MPU in use
6. Projected active population
Total active Locomotive and MPU population / year
7. Non-propulsion Energy Use
Energy use for non-propulsion activities
Metro, Light Rail, High-speed, Suburban and Main-line Service
8. Fuel and Electricity usage
Fuel and Electricity
Consumption/yr
Technology
Notes: In step 2 and 4: The turquoise boxes indicates information taken from previous steps

## Slide 26
Passenger
Freight
Waterborne passenger and freight transport
1. Base-year use patterns
Average kms travelled per TEU and passenger
Mix of use patterns
Macro Scenario
GDP
Urbanization
Population
On-road and rail private and mass-transit travel mix
Sea-going vessels
Self-propelled inland waterways
Push-barges inland waterways
Passenger Service
2. Projected travel distance
Propulsion unit mix
Future passenger-km and TEU-km travelled / year
Modal shift assumptions
Future Expansion plans
Future Pass & Freight movements
5. Projected barge, vessel and tug population usage and changes
Annual replacement
Unit sales per year
Mortality calc.
Load capacity
Fuel Efficiency
Per unit
3. Loading Factors
Total vessel loading and usage
4. Vessel / barge
configuration
TEU per unit and route type
Propulsion units in use
6. Projected active population
Total active vessel population / year
7. Non-propulsion Energy Use
Energy use for non-propulsion activities
Inland waterways and coastal shipping
8. Fuel usage
Fuel
Consumption/yr
Technology
Notes: In step 2 and 4: The turquoise boxes indicates information taken from previous steps

## Slide 27
1. Representative sample of scheduled flights in recent year
Civil Aviation
2. Base-year use patterns
LTO and CCD distances by aircraft type
Mix of use patterns
Macro Scenario
GDP
Urbanization
Population
On-road, water and rail private and mass-transit travel mix
National
Passenger
National
Freight
International
Passenger
International
Freight
3. Projected travel distance
Aircraft mix
Future passenger-km and freight ton-km travelled / year
Modal shift assumptions
Future Expansion plans
Future Pass & Freight movements
5. Projected Aircraft population usage and operation
Annual replacement
Unit sales per year
Mortality calc.
Load capacity
Fuel Efficiency
Per unit
4. Loading Factors
Aircraft loading and usage
7. Projected active population
Total active vessel population / year
8. Emissions and Energy Calculation
EMEP / EEA
Emissions
model
National Passenger & Freight, International Passenger & Freight
9. Fuel usage and emissions
Fuel
Consumption/yr
Technology
6. Economics
CAPEX, OPEX, Maintenance
Fuel Personnel
NOx emissions
SOx
emissions
CO emissions
HC emissions
PM emissions
CO2 emissions
Notes: In step 2 and 4: The turquoise boxes indicates information taken from previous steps

## Slide 28: Nonresidential Module Methodology
Projects the change in activity in each sector, sub-sector and the corresponding increase in floor-space required to 2050
Determines the current energy intensity for each sector and sub-sector
Identifies applicable efficiency measures and new technology
Analyzes best policy mix to make investment attractive to private investors
Computes energy consumption and electricity supply sources
Calculates economic and financial outputs for each sector and sub-sector by year and marginal abatement costs

## Slide 29: Industry Module Methodology
Develops a demand model for each industry based on national consumption, imports and exports to 2050
Evaluates the needed mix of new and existing plants
Determines the processes used and intermediate products and estimates the current energy intensity and process emissions
Identifies applicable efficiency measures, technologies and process improvements
Analyzes best policy mix to make new plant build and efficiency measures attractive to private investors
Computes energy consumption, process emissions and electricity supply sources
Calculates economic and financial outputs for each sector and sub-sector by year and marginal abatement costs

## Slide 30: Thank You
jarogers@worldbank.org